## Slide 1: Cyclic Redundancy Check (CRC-32)
Network Integrity & Error Detection Simulator
Team Members:
Ch. Munna (2503A520Q2)
Ved Prakash (2503A520Q2)
Vishnu (2503A520Q3)
Samvarsh (2503A520Q5)
Showrya (2503A520Q6)

## Slide 2: The Problem: Data Corruption in Networks
• Data Link / Physical Layer transmissions are prone to noise.
• Attenuation and Electromagnetic Interference (EMI) can alter signals.
• A single bit flip (0 ➔ 1) can completely corrupt a packet payload.
• Reliable systems require robust Error Detection schemes to ensure data integrity before passing packets up the network stack.

## Slide 3: Why CRC? (Cyclic Redundancy Check)
• Far superior to Simple Parity Checks or Checksums.
• Mathematically based on Polynomial Division using Modulo-2 arithmetic.
• CRC-32 (used in IEEE 802.3 Ethernet & Wi-Fi) uses a 32-degree generator polynomial.
• Detects 100% of single-bit, double-bit, and odd-numbered errors, and highly efficient for burst errors.

## Slide 4: System Architecture (3 Phases)
1. SENDER: Processes data, computes polynomial division, and appends a 32-bit Frame Check Sequence (FCS) to the payload.
2. TRANSMISSION MEDIUM: The channel where packets travel and noise (error injection) can occur.
3. RECEIVER: Performs polynomial division on the received codeword to verify if the remainder is zero.

## Slide 5: Phase 1: Sender Checksum Generation
• Message converted to a binary bitstream M(x).
• Appended with 32 zero-bits: M(x) * x^32.
• Divided by the predefined Generator Polynomial G(x).
• The Remainder R(x) is the CRC-32 checksum.
• Transmitted Codeword T(x) = M(x) * x^32 + R(x).

## Slide 6: Phase 2: Network Transmission & Error Injection
• The packet T(x) traverses the simulated network channel.
• Error Simulation: We simulate channel interference by XORing a specific data bit with 1 (Bit-flipping).
• As a result, the received polynomial T'(x) may differ from the originally sent T(x).
• Even a 1-bit difference drastically alters the final CRC hash.

## Slide 7: Phase 3: Receiver Verification
• The receiver captures the bitstream T'(x).
• It strips the payload from the appended checksum.
• It recalculates the CRC on the payload using the exact same generator polynomial G(x).
• It then compares its calculated Remainder against the received Remainder (Syndrome calculation).

## Slide 8: The Syndrome Decision
If Local Remainder == Received Remainder:
➔ ACCEPT
➔ No corruption detected. Packet is passed to the Network Layer.
If Local Remainder != Received Remainder:
➔ REJECT
➔ Data corrupted. An ARQ (Automatic Repeat reQuest) mechanism is typically triggered to retransmit.

## Slide 9: Project Implementation Details
• Frontend Interface: Built with HTML5, CSS3, and Vanilla JavaScript.
• Algorithm: Implemented a standard IEEE 802.3 CRC-32 lookup table in JS for O(N) fast byte-wise computation.
• Encoding: Uses TextEncoder for accurate String-to-UTF-8 Byte conversion before binary parsing.
• UI/UX: Interactive DOM manipulation to visualize bit-flipping and packet validation in real-time.

## Slide 10: Conclusion
CRC-32 ensures high reliability across modern networks through deterministic bit-level error detection.
Thank You!
Questions?